## Slide 1: BioRobotics

## Slide 2
What is Galvanic Skin Response?
Also known as Electrodermal Activity (EDA) or Skin Conductance
Core Concept
GSR measures the electrical conductance of the skin, which varies with sweat gland activity controlled by the sympathetic nervous system.
Emotional arousal → Sympathetic activation → Sweat secretion → Increased skin conductance
The response is involuntary and difficult to consciously control, making it a reliable indicator of autonomic arousal.
Key Facts
Signal Source
Eccrine sweat glands
Controlled By
Sympathetic nervous system
Reflects
Psychological/physiological arousal
Amplitude
0.1 - 30 μS (microsiemens)
Response Latency
1-3 seconds after stimulus

## Slide 3
Skin Anatomy & Sweat Glands
The physiological basis of electrodermal activity
Eccrine Sweat Glands
• Highest density on palms and soles • ~2,000-4,000 glands per cm² on palm • Respond to emotional stimuli • Innervated by sympathetic nervous system • Secrete sweat containing electrolytes
Why the Palms?
• Highest concentration of eccrine glands • Most sensitive to emotional stimuli • Easy electrode placement • Minimal interference from movement • Standard measurement location
Measurement Principle
A small constant voltage (typically 0.5V DC) is applied between two electrodes. As sweat fills the ducts, the ionic solution creates conductive pathways, increasing skin conductance. This change is measured in microsiemens (μS).

## Slide 4
Tonic vs Phasic Components
Two distinct aspects of the GSR signal
Tonic Component
Skin Conductance Level (SCL)
• Slow-changing baseline conductance • Changes over minutes to hours • Reflects general arousal state • High individual variability • Typically 2-20 μS range • Useful for overall stress levels
Think of it as the "background" arousal level
Phasic Component
Skin Conductance Response (SCR)
• Rapid, event-related changes • Onset 1-3 seconds after stimulus • Duration 1-5 seconds • Amplitude 0.1-1.0 μS typical • More consistent across individuals • Used for event-related analysis
Think of it as "spikes" in response to events

## Slide 5
SCR Characteristics
Anatomy of a skin conductance response
Key Parameters
Latency
1-3 seconds
Time from stimulus to response onset
Rise Time
1-3 seconds
Time from onset to peak
Amplitude
0.1-1.0 μS
Peak minus baseline
Recovery
2-10 seconds
Return to 50% of amplitude

## Slide 6
GSR Signal Characteristics
Technical parameters for recording
Parameter | Value | Notes
Measurement Unit | Microsiemens (μS) | Conductance = 1/Resistance
Typical Range | 0.1 - 30 μS | High individual variability
Frequency Content | DC - 5 Hz | Very low frequency signal
Sample Rate | 10 - 100 Hz | Lower than EMG/EOG required
Response Latency | 1 - 3 seconds | Relatively slow response
Electrode Coupling | DC (essential) | Must capture slow changes
Electrode Sites | Palmar surface | Fingers or palm

## Slide 7
GSR vs EMG vs EOG
Property | GSR | EMG | EOG
Signal Source | Sweat gland activity | Muscle action potentials | Corneo-retinal potential
Frequency Range | DC - 5 Hz | 20 - 500 Hz | DC - 30 Hz
Typical Amplitude | 0.1 - 30 μS | 50 μV - 5 mV | 15 - 200 μV
Sample Rate Needed | 10 - 100 Hz | 1000+ Hz | 250 - 500 Hz
Response Latency | 1 - 3 seconds | ~50 ms | Immediate
Voluntary Control | Minimal | Full | Full
Primary Application | Arousal/stress | Movement/force | Gaze tracking
Note: GSR reflects autonomic (involuntary) nervous system activity, while EMG and EOG reflect somatic (voluntary) control.

## Slide 8
Electrode Placement
Standard locations for GSR measurement
Common Electrode Sites
Palmar Surface (Fingers)
Most common - high sensitivity, easy access. Typically index and middle finger, medial phalanges.
Thenar/Hypothenar
Palm surface - useful when fingers unavailable. Good signal quality.
Plantar Surface (Feet)
Alternative when hands unavailable. Similar sweat gland density.
Best Practices
• Clean skin with water only (no alcohol)
• Use isotonic gel or pre-gelled electrodes
• Maintain consistent electrode spacing
• Secure electrodes to prevent movement
• Allow 2-5 minutes for stabilization
• Use non-dominant hand (less movement)
• Keep room temperature consistent

## Slide 9
Signal Quality Considerations
Common issues and solutions
Issue | Cause | Solution
No signal / flat line | Poor electrode contact | Check gel, clean skin, secure electrodes
Excessive noise | Movement artifacts | Stabilize hand, reduce cable movement
Rapid baseline drift | Temperature changes | Control room temperature, allow stabilization
Very low amplitude | Dry skin | Hydrate electrodes, ensure proper gel contact
60 Hz interference | Power line noise | Move cables away from power sources
Sudden jumps | Electrode shift | Resecure electrodes, check connections
Important: Do NOT use alcohol to clean skin before GSR measurement - it dries the skin and reduces conductance.

## Slide 10
Decomposing Tonic and Phasic
Separating baseline from event-related responses
Common Decomposition Methods
Low-pass Filtering
Apply very low cutoff (~0.05 Hz) to extract tonic. Subtract from original for phasic.
Pro: Simple
Con: Less accurate
Through-to-Peak
Find local minima (troughs) and maxima (peaks) to identify discrete SCRs.
Pro: Intuitive
Con: Threshold dependent
Continuous Decomposition
Model-based approach using deconvolution to estimate underlying driver signal.
Pro: Most accurate
Con: Complex
For this lab, we'll use simple baseline correction and peak detection for SCR analysis.

## Slide 11
Feature Extraction
Quantifying GSR for analysis
Tonic Features (SCL)
• Mean SCL - Average conductance level
• SCL Range - Max minus min
• SCL Slope - Rate of change over time
• SCL Variance - Signal variability
Phasic Features (SCR)
• SCR Count - Number of responses
• SCR Amplitude - Peak height
• SCR Latency - Time to peak
• SCR Rise Time - Onset to peak duration
Combined / Derived Features
• Area Under Curve (AUC) - Total response magnitude over time window • NS-SCR Rate - Non-specific SCRs per minute (responses without clear stimulus) • SCR/SCL Ratio - Phasic activity relative to tonic level • Recovery Time - Time for signal to return to baseline

## Slide 12
GSR Applications Overview
1
Stress & Anxiety
Workplace wellness, mental health
2
Lie Detection
Forensic and security
3
UX Research
Product testing, advertising
4
Clinical Biofeedback
Anxiety, PTSD treatment
5
Affective Computing
Emotion-aware AI systems

## Slide 13
Stress & Anxiety Monitoring
Continuous assessment of psychological state
How It Works
GSR increases with psychological stress due to sympathetic nervous system activation: • Work deadlines → Elevated SCL • Social anxiety → Increased SCR frequency • Cognitive load → Higher baseline + more responses • Emotional events → Clear SCR peaks Wearable devices now incorporate GSR sensors for continuous stress tracking.
Use Cases
• Workplace wellness programs
• Mental health monitoring
• Performance optimization
• Sleep quality assessment
• Meditation feedback
• PTSD episode detection

## Slide 14
Lie Detection (Polygraph)
The controversial but widespread application
The Theory
Deception causes emotional arousal (fear, guilt) which triggers autonomic responses including increased skin conductance. GSR is one of several measures in a polygraph.
Limitations
• Measures arousal, not deception • Innocent people may show responses • Can be beaten by countermeasures • Not admissible in most courts • ~85-90% accuracy at best
Modern research focuses on concealed information tests (CIT) and machine learning approaches, but fundamental limitations remain.

## Slide 15
UX Research & Affective Computing
Measuring unconscious user responses
Users often can't articulate their emotional responses. GSR provides objective data about engagement, frustration, and excitement that surveys miss.
Website/App Testing
Identify frustrating UI elements
Ad Effectiveness
Measure emotional impact of content
Gaming
Optimize difficulty and engagement
Adaptive Interfaces
Systems that respond to user state
Clinical Biofeedback
GSR biofeedback helps patients with anxiety disorders, PTSD, and phobias learn to recognize and control their arousal through real-time feedback.

## Slide 16
Why Experimental Design Matters
The foundation of valid scientific conclusions
Without proper experimental design, we cannot determine if observed effects are real or due to chance, bias, or confounding factors.
1
Control
Manipulate only what you intend to test
2
Randomization
Reduce systematic bias
3
Replication
Ensure effects are repeatable
4
Validity
Measure what you claim to measure

## Slide 17
Variables in Experiments
Independent, dependent, and confounding
Independent Variable (IV)
What you manipulate
• Task difficulty • Stimulus type • Condition order • Trial parameters
Dependent Variable (DV)
What you measure
• Mean SCL • SCR count • SCR amplitude • Response time
Confounding Variables
What you control for
• Time of day • Room temperature • Caffeine intake • Practice effects
Example:
"Does cognitive load increase skin conductance?"
IV: Task type (rest, easy, hard) | DV: Mean SCL, SCR count | Control: Same time, room, instructions

## Slide 18
Within vs Between Subjects
Two fundamental approaches to experimental design
Within-Subjects Design
Same participants in ALL conditions
Advantages:
• Fewer participants needed • Controls for individual differences • More statistical power
Disadvantages:
• Order/practice effects • Fatigue • Longer sessions
Between-Subjects Design
Different participants in EACH condition
Advantages:
• No order effects • Shorter individual sessions • No carryover
Disadvantages:
• More participants needed • Individual differences add noise • Less statistical power

## Slide 19
Counterbalancing
Controlling for order effects in within-subjects designs
Problem: If everyone does A → B → C, we can't tell if differences are due to the condition or the order.
Solution: Counterbalancing - vary the order across participants
Full Counterbalancing
Every possible order (n! permutations)
Participant | Order
P1 | A → B → C
P2 | A → C → B
P3 | B → A → C
P4 | B → C → A
P5 | C → A → B
P6 | C → B → A
Latin Square
Each condition once in each position
Participant | Order
P1, P4, P7... | A → B → C
P2, P5, P8... | B → C → A
P3, P6, P9... | C → A → B
More practical for many conditions

## Slide 20
The Stroop Effect
A classic demonstration of cognitive interference
Named after John Ridley Stroop (1935), this effect demonstrates interference when the brain processes conflicting information.
Congruent
Word matches ink color
RED
BLUE
GREEN
Incongruent
Word conflicts with ink color
RED
BLUE
GREEN
The Task: Name the INK COLOR, ignore the word meaning
Reading is automatic - we can't help but read the word. When it conflicts with the color, our brain must suppress the automatic response. This cognitive conflict increases response time, errors, and physiological arousal (including GSR).

## Slide 21
Stroop Task Parameters
Variables you can manipulate to control difficulty
Number of Trials
20 - 100+
More trials = more data, but fatigue increases. Trade-off between power and burden.
Congruent/Incongruent Ratio
50/50 to 25/75
Higher incongruent ratio = more difficult. Manipulating expectation affects load.
Inter-Stimulus Interval (ISI)
500ms - 3000ms
Shorter ISI = faster pace, more demand. Longer ISI allows recovery.

## Slide 22
Paired t-tests
Comparing conditions in within-subjects designs
After collecting GSR data, we need to determine if differences are statistically significant.
Paired t-test
Use when comparing the SAME participants across two conditions
• Compares each participant's score in Condition A to their score in Condition B • Controls for individual differences (each person is their own control) • More powerful than independent t-test when assumptions are met • Null hypothesis: The mean difference between conditions = 0
Example: Is mean SCL during Stroop > mean SCL during Rest?
H₀: μ_Stroop - μ_Rest = 0 vs H₁: μ_Stroop - μ_Rest ≠ 0
If p < 0.05, we reject H₀ and conclude the conditions differ significantly.

## Slide 23
Interpreting Results
Understanding p-values and effect sizes
p-value
Probability of observing results this extreme if H₀ is true. • p < 0.05: "Significant" • p < 0.01: More confident • p < 0.001: Highly significant
Effect Size (Cohen's d)
Magnitude of difference, independent of sample size. • |d| < 0.2: Small • |d| ≈ 0.5: Medium • |d| > 0.8: Large
Example Report
"Mean SCL was significantly higher during the Stroop task (M = 8.2 μS, SD = 2.1) compared to rest (M = 5.4 μS, SD = 1.8), t(19) = 4.32, p < .001, d = 0.96."
• Reports both conditions' means and SDs • States test statistic t(df) and p-value • Includes effect size (d = 0.96 is large)

## Slide 24
References & Further Reading
Textbook
Boucsein, W. (2012). Electrodermal Activity (2nd ed.). Springer.
Methods
Braithwaite, J.J., et al. (2013). A Guide for Analysing Electrodermal Activity.
Stroop
Stroop, J.R. (1935). Studies of interference in serial verbal reactions.
Software
Ledalab - http://www.ledalab.de/ (MATLAB toolbox)
Python
NeuroKit2 - https://neuropsychology.github.io/NeuroKit/